## Slide 1: Robot Autonomy
Dr. risman adnan mattotorang
Telkom university

## Slide 2: W6: Motion planning II: sampling-based methods
Principles of Robot Autonomy I

## Slide 3: Motion Planning
Compute sequence of actions that drives a robot from an initial condition to a terminal condition while avoiding obstacles, respecting motion constraints, and possibly optimizing a cost function
Aim
  Learn about sampling-based motion planning algorithms
Readings:
  S. LaValle. Planning Algorithms. Chapter 5.

## Slide 4: Configuration space

## Slide 5: Motion Planning Algorithms
Key point: motion planning problem described in the real-world, but it really lives in another space - the configuration (C-)space!
Two main approaches to continuous motion planning:
  Combinatorial planning: constructs structures in the C-space that discretely and completely capture all information needed to perform planning
  Sampling-based planning: uses collision detection algorithms to probe and incrementally search the C-space for a solution, rather than completely characterizing all of the structure

## Slide 6: Sampling-based Motion Planning
Limitations of combinatorial approaches stimulated the development of sampling-based approaches
Abandon the idea of explicitly characterizing and
Instead, capture the structure of by random sampling
Use a black-box component (collision checker) to determine which random configurations lie in
Use such a probing scheme to build a roadmap and then plan a path
Reference: LaValle, S. M. Motion planning. 2011.

## Slide 7: Sampling-based Motion Planning
Pros:
Conceptually simple
Relatively-easy to implement
Flexible: one algorithm applies to a variety of robots and problems
Beyond the geometric case: can cope with complex differential constraints, uncertainty, etc.
(Mild) cons:
Unclear how many samples should be generated to retrieve a solution
Cannot determine whether a solution does not exist

## Slide 8: Outline
The geometric case
The kinodynamic case
Alternative sampling strategies (de-randomized; biased)

## Slide 9: Outline
The geometric case
The kinodynamic case
Alternative sampling strategies (de-randomized; biased)

## Slide 10: Review of sampling-based methods
Traditionally, two major approaches:
Probabilistic Roadmap (PRM): graph-based
  Multi-query planner, i.e., designed to solve multiple path queries on the same scenario
  Original version: [Kavraki et al., ‘96]
  “Lazy” version: [Bohlin & Kavraki, ‘00]
  Dynamic version: [Jaillet & T. Simeon, ‘04]
  Asymptotically optimal version: [Karaman & Frazzoli, ‘11]
Rapidly-exploring Random Trees (RRT): tree-based
  Single-query planner
  Original version: [LaValle & Kuffner, ‘01]
  RDT: [LaValle, ‘06]
  SRT: [Plaku et al., ‘05]
  Asymptotically optimal version [Karaman & Frazzoli, '11]

## Slide 11: Probabilistic roadmaps (PRM)
A multi-query planner, which generates a roadmap (graph) , embedded in the free space
Preprocessing step:
Sample a collection of configurations ; discard configurations leading to collisions
Draw an edge between each pair of samples such that and straight-line path between and is collision free
Given a query , connect them to and find a path on the roadmap

## Slide 12: Rapidly-exploring random trees (RRT)
A single-query planner, which grows a tree , rooted at the start configuration , embedded in
Algorithm works in iterations:
Sample configuration
2. Find nearest vertex in to
Generate configuration in direction of from , such that
Update tree:
Occasionally, set to be the target vertex ; terminate when

## Slide 13: Rapidly-exploring random trees (RRT)
RRT is known to work quite well in practice
Its performance can be attributed to its Voronoi bias:
  Consider a Voronoi diagram with respect to the vertices of the tree
  For each vertex, its Voronoi cell consists of all points that are closer to that vertex than to any other
  Vertices on the frontier of the tree have larger Voronoi cells – hence sampling in those regions is more likely

## Slide 14: Theoretical guarantees: probabilistic completeness
Question: how large should the number of samples be? We can say something about the asymptotic behaviour:
Kavraki et al. 96: PRM, with = const, will eventually (as → ∞) find a solution if one exists
LaValle, 98; Kleinbort et al., 18: RRT will eventually(as → ∞) find a solution if one exists
* Unless stated otherwise, the configuration space is assumed to be the -dimensional Euclidean unit hypercube [0,1]d, with 2 ≤ ≤ ∞

## Slide 15: Theoretical guarantees: Quality
Question: what can be said about the quality of the returned solution for PRM and RRT, in terms of length, energy, etc.?
Nechushtan et al. (2011) and Karaman and Frazzoli (2011) proved that RRT can produce arbitrarily-bad paths with non-negligible probability: for example, RRT would prefer to take the long (red) way

## Slide 16: Theoretical guarantees: Quality
Karaman and Frazzoli in 2011 provided the first rigorous study of optimality in sampling-based planners:
Theorem: The cost of the solution returned by PRM converges, as → ∞, to the optimum, when , where only depends on
KF11 also introduced an asymptotically optimal variant of RRT called RRT* (right)
Result was later updated to [Solovey et al. 2019]:
Now back to 1/d [preprint, Lukyanenko et al. 2021]

## Slide 17: Observations
PRM-like motion planning algorithms
  For a give number of nodes , they find “good” paths
  ...however, require many costly collision checks
RRT-like motion planning algorithms
  Finds a feasible path quickly
  ...however, the quality of that path is, in general, poor
  “traps” itself by disallowing new better paths to emerge - RRT* performs local label correction as samples are added to help remedy this

## Slide 18: Fast Marching Tree Algorithm (FMT*)
Key idea: run dynamic programming (DP) on sampled nodes, skipping any step in which the attempted connection causes a collision
  lazy DP operator:
Laziness introduces “suboptimal” connections, but such connections are vanishingly rare and FMT* is asymptotically optimal
Ratio of # of collision-checks for FMT* versus PRM* goes to zero!
Reference: Janson et al. Fast Marching Tree: A Fast Marching Sampling-Based Method for Optimal Motion Planning in Many Dimensions. 2015

## Slide 19: Sampling-based planning: summary
Sampling-based planners transform the difficult global problem into a large set of local and easy problems
A key ingredient is collision detection, which is conceptually easy, as it can be solved in the workspace (2D or 3D)
Local planning (edge validation) is typically performed by dense sampling of path and collision detection
Another key ingredient is nearest-neighbor search: given a query point find its nearest neighbor(s) within a set of points -- also well studied theoretically and practically

## Slide 20: Outline
The geometric case
The kinodynamic case
Alternative sampling strategies (de-randomized; biased)

## Slide 21: Flexible trajectories in kinodynamic motion planning
https://github.com/rikkimelissa/baxter_throw
Rikki Valverde, Northwestern University

## Slide 22: Kinodynamic motion planning for vehicle high speed maneuvering
Yanbo Li

## Slide 23: Kinodynamic Planning
Kinodynamic motion planning problem: in addition to obstacle avoidance, paths are subject to differential constraints
The robot operates in the state space
To move the robot applies control
Motion needs to satisfy the system’s constraints:
Reference: Schmerling and Pavone. Kinodynamic Planning. 2019

## Slide 24: Forward-propagation-based algorithms
RRT can be extended to the kinodynamic case in a relatively easy way:
Draw a random state and find its nearest neighbor
Sample a random control ∈ and random duration
Forward propagate the control for time from
Reference: Kleinbort et al. Probabilistic completeness of RRT for geometric and kinodynamic planning with forward propagation. 2018.

## Slide 25: Steering-based algorithms
When efficient online steering subroutines exist, kinodynamic planning algorithms may take advantage of this domain knowledge
Reference: E. Schmerling et al. Optimal SamplingBased Motion Planning under Differential Constraints: the Driftless Case. 2015
Connect samples by using an optimal trajectory (steering problem)
Use reachable sets to find nearest neighbors

## Slide 26: Outline
The geometric case
The kinodynamic case
Alternative sampling strategies (de-randomized; biased)

## Slide 27: Should probabilistic planners be probabilistic?
Key question: would theoretical guarantees and practical performance still hold if these algorithms were to be de-randomized, i.e., run on deterministic samples?
Important question as de-randomization would:
Ease certification process
Ease use of offline computation
Potentially simplify several operations (e.g., NN search)

## Slide 28: Designing “good” sequences
Key facts:
There exist deterministic sequences with D(S) of order 0(n-1/d) , referred to as low-dispersion sequences
Sequences minimizing ℓ2-dispersion only known for d = 2
ℓ2-dispersion: For a finite set S of points contained in X ⊂ ℝd, its ℓ2-dispersion D(S) is defined as

## Slide 29: Optimality of deterministic planning
Optimality: Let denote the arc length of the path returned with samples. Then if
Samples set S has dispersion for some > 0,
n1/d rn , then , where �∗ is the cost of an optimal path

## Slide 30: Deterministic sampling-based motion planning
Asymptotic optimality can be achieved with deterministic sequences and with a smaller connection radius
Deterministic convergence rates: instrumental to the certification of sampling-based planners
Computational and space complexity: under some assumptions, arbitrarily close to theoretical lower bound
Deterministic sequences appear to provide superior performance
Reference: Janson et al. Deterministic Sampling-Based Motion Planning: Optimality, Complexity, and Performance. 2018

## Slide 31: Biased sampling for SBMP
Potential issue with uniform sampling: narrow corridors in C-space require many samples to identify/traverse
Key idea: bias sampling towards suspected such challenging regions of C-space
Biased sampling distributions can be handconstructed and/or adapt online (e.g., Hybrid Sampling PRM), or learned from prior experience solving similar planning problems
References: Hsu et al. Hybrid PRM sampling with a cost-sensitive adaptive strategy. 2005. Ichter et al. Learned Critical Probabilistic Roadmaps for Robotic Motion Planning. 2020

## Slide 32
Which of these two roadmaps has been created by RRT ?

## Slide 33
How many of the red sample points could lead to new node in the roadmap constructed by RRT?

## Slide 34: Next Lecture : Robotic Sensors and Introduction to Computer Vision